HOW TO MIX SOLUTIONS

|  | Assess the risks to yourself and others |  |
| --- | --- | --- |
|  | Read the instructions on the label |  |
|  | Read the product safety data sheet |  |
|  | Select the containers and equipment |  |
|  | Identify the mixing ratio |  |
|  | Pour the amount of water required into a container |  |

HOW TO MIX SOLUTIONS (continued)

|  | Pour the amount of chemical into a measured container |  |
| --- | --- | --- |
|  | Pour the chemical into the water and mix |  |
|  | Store the solution in a sealed, marked container |  |

HOW YOU SHOULD CLEAN TOILETS

|  | Flush toilets |  |
| --- | --- | --- |
|  | Use toilet brush to lower toilet water level |  |
|  | Apply toilet cleanser to inside surfaces and leave to soak |  |
|  | Use colour-coded cloths to clean all exterior surfaces |  |
|  | Use toilet brush to clean inside toilet bowl Flush toilet |  |
|  | Rinse toilet |  |
|  | Check all fixtures and fittings have been cleaned |  |
|  | Refill or replace consumables Note any faults or problems |  |

HOW YOU SHOULD CLEAN URINALS

|  | Flush urinals Turn off automatic flushing if possible |  |
| --- | --- | --- |
|  | Clear waste outlet and channel of debris |  |
|  | Clean entire face of urinal with cleaning agent |  |
|  | Use colour-coded cloths to clean all exterior surfaces |  |
|  | Use toilet brush to clean inside the urinal Use bottle brush to clean grating |  |
|  | Rinse toilet brush and then urinal Turn on auto flush if applicable |  |
|  | Ensure all fixtures and fittings have been cleaned |  |
|  | Replace/refill consumables Note any faults or problems |  |

HOW YOU SHOULD CLEAN WASH HAND BASINS

|  | Remove soap etc from basins Remove debris from plughole |  |
| --- | --- | --- |
|  | Wipe the entire inside of the bowl Clean inside the overflow |  |
|  | Rinse thoroughly |  |
|  | Work from clean to dirty areas Wipe all surrounding areas |  |
|  | Polish chrome/stainless steel (e.g. taps) | 012 K8 |
|  | Replace consumables |  |
|  | Note any faults/problems |  |

HOW YOU SHOULD CLEAN WASHROOM FURNITURE

|  | Clean and polish mirrors |  |
| --- | --- | --- |
|  | Clean cubicles and splash backs |  |
|  | Clean dispensers and bins |  |
|  | Note any faults/problems |  |
|  | Replace consumables |  |

HOW YOU SHOULD REPLENISH CONSUMABLES

|  | Check the level of resources left in dispensers |  |
| --- | --- | --- |
|  | Refill to the recommended level Follow the manufacturers’ instructions when refilling or replacing consumables |  |
|  | Always use the correct colour coded consumable items if applicable e.g. Sanitary/waste bags |  |
|  | Do not overfill or leave too many consumable items |  |

HOW YOU SHOULD PREPARE TO CLEAN FLOORS MANUALLY

|  | Consider the risks to self and others |  |
| --- | --- | --- |
|  | Decide the best method to clean the floor |  |
|  | Pick up large items of litter |  |
|  | Move furniture and other moveable objects |  |
|  | Check/report damage Remove sticky solids |  |

HOW YOU SHOULD MANUALLY PASS DRY MOPS OVER FLOORS

|  | Mop edges and corners |  |
| --- | --- | --- |
|  | Begin at furthest point from the exit |  |
|  | Work on small sections when covering large areas |  |
|  | Work with a continuous pass |  |
|  | Overlap the previous pass on each turn |  |
|  | Check mop frequently |  |

HOW YOU SHOULD BRUSH SWEEP SEMI HARD AND HARD FLOORS MANUALLY

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Select the brush to suit the floor type and task |  |
|  | Sweep edges and corners |  |
|  | Sweep main floor |  |
|  | Sweep dirt into piles for removal |  |
|  | Complete manual cleaning of floor |  |

HOW YOU SHOULD BRUSH SCRUB SEMI HARD AND HARD FLOORS MANUALLY

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Select and prepare the solution |  |
|  | Select the brush and equipment |  |
|  | Apply the solution |  |
|  | Pass scrubbing brush over floor |  |
|  | Remove solution |  |
|  | Complete manual cleaning of floor |  |

HOW YOU SHOULD MANUALLY PASS DAMP MOPS OVER FLOORS

|  | Start at furthest point from exit |  |
| --- | --- | --- |
|  | Apply the solution |  |
|  | Start cleaning at the edges |  |
|  | Work in continuous strokes |  |
|  | Overlap each pass |  |
|  | Work on small sections when covering large areas |  |
|  | Rub stubborn marks |  |
|  | Wipe splashes from skirting boards as they occur |  |

HOW YOU SHOULD REMOVE SPILLAGES FROM FLOORS

|  | Identify the spillage and floor type |  |
| --- | --- | --- |
|  | Pick up solid items |  |
|  | Remove semi solids |  |
|  | Remove water based spills |  |
|  | Remove body fluids |  |

HOW YOU SHOULD REMOVE SPILLAGES FROM FLOORS (continued)

|  | Check for stains |  |
| --- | --- | --- |
|  | Complete manual cleaning of floor |  |

HOW YOU SHOULD SUCTION CLEAN FLOORS

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Decide which attachments to use |  |
|  | Fit and adjust attachments |  |
|  | Move furniture and other moveable objects |  |
|  | Clean edges and corners |  |
|  | Pass over the floor |  |
|  | Complete manual cleaning of floor |  |

HOW YOU SHOULD COMPLETE MANUAL CLEANING OF FLOORS

|  | Allow floor to dry if applicable |  |
| --- | --- | --- |
|  | Replace furniture and other moveable objects |  |
|  | Clean equipment and return it to store |  |

HOW YOU SHOULD DRY DUST FURNITURE, FITTINGS AND VERTICAL SURFACES

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Select the duster |  |
|  | Dust the item |  |
|  | Refold the duster frequently and replace as necessary |  |
|  | Clean, check and return equipment to store |  |

HOW YOU SHOULD DAMP DUST FURNITURE, FITTINGS AND VERTICAL SURFACES

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Select and prepare the solution or polish |  |
|  | Damp wipe the surface |  |
|  | Rinse cloth frequently |  |
|  | Clean, check and return equipment to store |  |

HOW YOU SHOULD POLISH FURNITURE, FITTINGS AND VERTICAL SURFACES

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Select and prepare the POLISH |  |
|  | Apply polish |  |
|  | Allow to dry |  |
|  | Buff |  |
|  | Clean, check and return equipment to store |  |

HOW YOU SHOULD CLEAN HANDRAILS AND BALUSTRADES

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Select cleaning method |  |
|  | Select and prepare the solution if applicable |  |
|  | Apply solution (if applicable) |  |
|  | Rinse or re-fold cloth frequently |  |
|  | Allow to dry |  |
|  | Clean, check and return equipment to store |  |

HOW YOU SHOULD PREPARE TO CLEAN WALLS

|  | Consider the risks to self and others |  |
| --- | --- | --- |
|  | Identify type of wall |  |
|  | Remove pictures etc |  |
|  | Protect surrounding areas |  |
|  | Suction clean the wall |  |
|  | Report staining and graffiti |  |
|  | Clean equipment and return it to store |  |

HOW YOU SHOULD WASH GROUND-IN SOIL FROM WALLS

Note: Where the wall is made of glass treat it as a window and see Section O: Clean Furniture, Fittings & Vertical Surfaces Manually

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Prepare reach equipment |  |
|  | Select and prepare the solution |  |
|  | Test for Colourfastness |  |
|  | Select the applicator |  |
|  | Apply solution to heavily soiled areas |  |

HOW YOU SHOULD WASH GROUND-IN SOIL FROM WALLS (continued)

|  | Apply solution |  |
| --- | --- | --- |
|  | Rinse |  |
|  | Check for stains |  |
|  | Clean, check and return equipment to store |  |

HOW YOU SHOULD REMOVE GRAFFITI

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Prepare reach equipment |  |
|  | Identify graffiti material |  |
|  | Select and prepare the solution |  |
|  | Test for Colourfastness |  |
|  | Select the applicator |  |
|  | Apply solution |  |

HOW YOU SHOULD REMOVE GRAFFITI (continued)

|  | Allow contact time |  |
| --- | --- | --- |
|  | Clean area |  |
|  | Wash off solution and rinse |  |
|  | Check for stains |  |
|  | Clean, check and return equipment to store |  |

HOW YOU SHOULD CLEAN HIGH WALLS

|  | Consider the risks to self and others |  |
| --- | --- | --- |
|  | Use reach tools first |  |
|  | Erect access equipment safely |  |
|  | Use access equipment safely |  |
|  | Use Cleaning machinery safely |  |

HOW YOU SHOULD CLEAN CURTAINS & UPHOLSTERY USING A SUCTION CLEANER

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Prepare area |  |
|  | Prepare suction cleaner |  |
|  | Vacuum curtains |  |
|  | Vacuum upholstery |  |
|  | Replace loose cushions |  |
|  | Clean, check and return equipment to store |  |

HOW YOU SHOULD CLEAN WINDOWS & GLASS

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Remove dried paint or debris |  |
|  | Select and prepare the solution |  |
|  | Clean top and sides of frames |  |
|  | Clean glass |  |
|  | Remove water and dirt from glass |  |

HOW YOU SHOULD CLEAN WINDOWS & GLASS (Continued)

|  | Remove water and dirt from frame |  |
| --- | --- | --- |
|  | Clean bottom of frame |  |
|  | Dry frame |  |
|  | Clean, check and return equipment to store |  |

HOW YOU SHOULD CLEAN COMPUTERS

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Check availability for cleaning |  |
|  | Prepare area |  |
|  | Remove dust and debris |  |
|  | Prepare solution |  |
|  | Apply solution |  |
|  | Clean screen |  |
|  | Clean keyboard |  |

HOW YOU SHOULD CLEAN COMPUTERS (Continued)

|  | Replace plug |  |
| --- | --- | --- |
|  | Clean, check and return equipment to store |  |

|  | Replace plug |  |
| --- | --- | --- |
|  | Clean, check and return equipment to store |  |

HOW YOU SHOULD CLEAN TELEPHONES

|  | Carry out preparation tasks |  |
| --- | --- | --- |
|  | Check availability for cleaning |  |
|  | Prepare solution |  |
|  | Apply solution |  |
|  | Wipe telephone |  |
|  | Clean flex |  |
|  | Clean surround |  |
|  | Clean, check and return equipment to store |  |

TOOLS & EQUIPMENT FOR CLEANING TOILETS & WASHROOMS

Before using any Tools or Equipment the cleaner must understand the contents of the following sections of this reference material:

A: Health & Safety, B: Identify Hazards & Security, and C: Reduce Risks

|  | Floors All standard equipment for cleaning hard floors See section N2: Tools & Equipment to Clean Floors Manually |  |
| --- | --- | --- |
|  | Walls All standard equipment for cleaning walls See section S: Materials & Equipment for Cleaning Surfaces up to a Maximum Height of 4 Metres |  |
|  | Colour Coded Cloths Used to wash, rinse and dry surfaces Different colour used for each process to prevent cross contamination Colour used may vary according to company’s colour code practice |  |
|  | Colour Coded Scouring Pads Used to remove stubborn marks Different colours used according to area being cleaned to prevent cross contamination Colour used may vary according to company’s colour code practice |  |

|  | Colour Coded Gloves Used to protect hands and prevent spread of germs Different colours used according to area being cleaned to prevent cross contamination Colour used may vary according to company’s colour code practice |  |
| --- | --- | --- |

TOOLS & EQUIPMENT FOR CLEANING TOILETS & WASHROOMS (continued)

|  | Colour Coded Bin Liners Used to hold refuse and debris Different grades and colours available to suit most types of refuse Refuse should be separated to prevent cross contamination Colour used may vary according to company’s colour code practice |  |
| --- | --- | --- |
|  | 7 Waste Bin Liners Used to line waste bins for ease of waste removal and cleanliness Different grades/weights available depending on likely contents |  |
|  | Toilet Brush and Holder Used to scrub toilet inside of toilets and urinals |  |
|  | Bottle Brush Used to clean inside of overflow and difficult to reach areas such as around taps |  |
|  | Paper Towels Used to dry chrome fittings and mirrors to prevent smears Easily disposable Can be colour coded if necessary |  |

To help with the confusion with dilution rates the following table should help you.

| 1:25 | 200ml per 5 litre | 1 cupful |
| --- | --- | --- |
| 1:50 | 100ml per 5 litre | ½ cupful |
| 1:100 | 50ml per 5 litre | 2 standard 5lt capfuls |
| 1:200 | 25ml per 5 litre | 1 standard 5lt capful |
| 1:300 | 17ml per 5 litre | 2 tablespoonful |
| 1:400 | 12.5ml per 5 litre | ½ capful |
| 1:500 | 10ml per 5 litre | 1 tablespoon |
| 1:1000 | 5ml per 5 litre | 1 teaspoon |
| 1 Teaspoonful | 5ml |  |
| 1 Tablespoon | 10ml |  |
| 1 standard 5lt capful | 24ml | Approx. 1 oz |
| 1 Cupful | 220ml | Approx. 8 oz |

The following charges show how to mix various common dilution rates in two separate containers (a trigger spray and a bucket).  A blank space indicates that the method of dispensing the product is impractical since the quantity would be either a very small fraction or a large number of measures.

|  | 1:5 1 part product to 5 parts water | 1:10 1 part product to 10 parts water | 1:15 1 part product to 15 parts water | 1:20 1 part product to 20 parts water |
| --- | --- | --- | --- | --- |
|  | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket |
| Precise amount of product | 100ml | 1000ml | 50ml | 500ml | 34ml | 333ml | 25ml | 250ml |
| 25ml dispenser pump | 4 | 40 | 2 | 20 | 1 ½ | 13.25 | 1 | 10 |
| 20ml cap | 5 | 50 | 2 ½ | 25 | 1 ¾ | 16.50 | 1 ¼ | 12 |

|  | 1:25 1 part product to 25 parts water | 1:30 1 part product to 30 parts water | 1:40 1 part product to 40 parts water | 1:50 1 part product to 50 parts water |
| --- | --- | --- | --- | --- |
|  | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket |
| Precise amount of product | 20ml | 200ml | 17ml | 117ml | 12.5ml | 125ml | 10ml | 100ml |
| 25ml dispenser pump | 1 | 8 | ¾ | 4.5 | ½ | 5 | ½ | 4 |
| 20ml cap | 1 | 10 | 1 | 5.75 | ¾ | 7 | ½ | 5 |

|  | 1:60 1 part product to 60 parts water | 1:75 1 part product to 75 parts water | 1:100 1 part product to 100 parts water | 1:125 1 part product to 125 parts water |
| --- | --- | --- | --- | --- |
|  | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket |
| Precise amount of product | 8.5ml | 84ml | 7ml | 67ml | 5ml | 50ml | 4ml | 40ml |
| 25ml dispenser pump | ½ | 3.25 | 1/3 | 2.75 | ¼ | 2 |  | 1.5 |
| 20ml cap | ½ | 4.25 | ½ | 3.25 | ¼ | 3 |  | 2 |

|  | 1:150 1 part product to 150 parts water | 1:200 1 part product to 200 parts water | 1:250 1 part product to 250 parts water | 1:500 1 part product to 500 parts water |
| --- | --- | --- | --- | --- |
|  | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket | 0.5 litre spray bottle | 5 litre bucket |
| Precise amount of product | 3.5ml | 34ml | 2.5ml | 25ml | 2ml | 20ml | 1ml | 10ml |
| 25ml dispenser pump |  | 1.25 |  | 1 |  | 0.75 |  | 0.5 |
| 20ml cap |  | 1.75 |  | 1.25 |  | 1 |  | 0.5 |