TYPES OF FLOORING

|  | Open Strand Woven Carpet |  |
| --- | --- | --- |
|  | Loop Woven Carpet |  |
|  | Thick Loop Woven Carpet |  |
|  | Cork Tiles |  |
|  | Linoleum |  |
|  | Rubber |  |

WHAT YOU SHOULD KNOW ABOUT FLOOR TYPES

This is a soft floor Used in homes and areas where low numbers of people walk Can be cleaned with suction machines fitted with rotating brushes Can be deep cleaned using the hot water extraction method

This is a soft floor Used in homes and offices where high numbers of people walk Can be cleaned with suction machines fitted with rotating brushes Can be deep cleaned using the hot water extraction method

This is a soft floor Used in areas where high numbers of people walk Can be damaged by brushes on cleaning machines Most suitable cleaning method is suction cleaning without brushes Can be deep cleaned using the hot water extraction method

This is a semi hard floor Used where good heat insulation is required Must be sealed to prevent water being absorbed Can be easily damaged by highly abrasive brushes and pads Most suitable cleaning method is damp cleaning Care must be taken not to strip too aggressively when removing seal

This is a semi hard floor Used to give warmth and quietness when walked on Must be polished to prevent water being absorbed Most suitable cleaning method is damp Can be easily damaged by highly abrasive brushes and pads Can be burnished to give a high gloss finish

This is a semi hard floor Used to give warmth and quietness when walked on and to provide a non-slip surface Must be polished to prevent water being absorbed Most suitable cleaning method is damp cleaning Can be easily damaged by highly abrasive brushes and pads Can be burnished to give a high gloss finish

TYPES OF FLOORS (Continued)

|  | Vinyl |  |
| --- | --- | --- |
|  | Wooden Boards |  |
|  | Parquet Floor |  |
|  | Ceramic Tiles |  |
|  | Quarry Tiles |  |

WHAT YOU SHOULD KNOW ABOUT FLOOR TYPES (continued)

This is a semi hard floor Used to give warmth and quietness when walked on and to provide an oil resistant and waterproof surface Most suitable cleaning method is damp cleaning Can be easily damaged by highly abrasive brushes and pads Can be burnished to give a high gloss finish None slip vinyl has abrasive particles in it which can make it very difficult to clean

This is a semi hard floor Used to give a natural appearance Must be polished or sealed to prevent water being absorbed Most suitable cleaning method is dry cleaning and polishing Can be easily damaged by highly abrasive brushes and pads Can be burnished to give a high gloss finish

This is a semi hard floor Used to give a patterned natural tile appearance Must be polished or sealed to prevent water being absorbed Most suitable cleaning method is dry cleaning and polishing Can be easily damaged by highly abrasive brushes and pads Can be burnished to give a high gloss finish

This is a hard floor Used to give a naturally cool floor although they are also excellent for conducting heat from under-floor heating Most suitable cleaning method is damp cleaning These tiles are VERY SLIPPERY when wet Can be easily damaged when heavy objects are dropped on them Can be burnished to give a high gloss finish

This is a hard floor Used to give a naturally cool floor although they are also excellent for conducting heat from under floor heating Must be sealed to prevent water being absorbed and can be polished Most suitable cleaning method is damp cleaning Can be easily damaged when heavy objects are dropped on them Can be burnished to give a high gloss finish

TYPES OF FLOORS (continued)

|  | Granite |  |
| --- | --- | --- |
|  | Marble |  |
|  | Sandstone |  |
|  | Slate |  |
|  | Concrete |  |

WHAT YOU SHOULD KNOW ABOUT FLOOR TYPES (continued)

This is a hard floor Used to give a naturally cold floor, is resistant to chemicals but noisy when walked upon Most suitable cleaning method is damp cleaning Can be burnished to give a high gloss finish, but this can produce a very slippery surface when dusty and wet

This is a hard floor Used to give a naturally cold floor, is resistant to chemicals but noisy when walked upon Most suitable cleaning method is damp cleaning Can be burnished to give a high gloss finish, but this can produce a very slippery surface when dusty and wet

This is a hard floor Used to give a naturally cool floor. Must be sealed to prevent water soaking in Most suitable cleaning method is damp cleaning

This is a hard floor Used to give a naturally cold floor, is resistant to chemicals and water but noisy when walked on Most suitable cleaning method is damp cleaning Can be burnished to give a high gloss finish but this can produce a very slippery surface when dusty and wet

This is a hard floor Used to give a naturally cold floor, it can be shaped and coloured to look like other types of floors Concrete must be sealed as it soaks up water and stains easily Most suitable cleaning method is damp cleaning Can be burnished to give a high gloss finish

# Text boxes

© B-Skill Ltd.

Permission to reproduce this material must be obtained from:

B-Skill Limited

Chaucer Buildings

57 Grainger Street

Newcastle upon Tyne

NE1 5JE

Tel: 0845 230 3736

Fax: 0845 230 4634

Designed in conjunction with Award Learning Services Ltd, Chelmsford

CLEANING BUILDING INTERIORS

Support Material for N/SVQ’s Level 2