BRUSHES AND PADS FOR CLEANING HARD AND SEMI HARD FLOORS

|  | Drive Board Fitted to rotary machines Pad is trapped by friction between board and floor Pad must be central under board to prevent wandering |  |
| --- | --- | --- |
|  | Porcupine Pad Holder Fitted to rotary machines Pad is gripped by the spikes on the holder Pad must be central under board to prevent wandering |  |
|  | Scrubbing Brush Fitted to rotary machines Bristles are strong nylon Suitable for wet or dry scrubbing any surface Most suitable for heavily soiled surfaces Also available for roller machines |  |
|  | Union Mix Polishing Brush Fitted to rotary machines Bristles are natural fibre Suitable for polishing and light scrubbing Suitable for most floors and in particular polished wood, marble, stone and tile Also available for roller machines |  |
|  | High Lustre Polishing Brush Fitted to rotary machines Bristles are soft nylon Suitable for final polishing to achieve shine Suitable for most floors where emulsion polish has been applied Also available for roller machines |  |

|  | Scrubbing / Stripping Brush Fitted to rotary machines Bristles are strong polypropylene with embedded abrasive particles Suitable for stripping any surface before applying seal or polish Also available for roller machines |
| --- | --- |

BRUSHES AND PADS FOR CLEANING HARD AND SEMI HARD FLOORS (continued)

|  | Scarifying Brush Fitted to rotary machines Bristles are steel Suitable for keying concrete or stone surfaces before sealing NOT suitable for semi hard surfaces Also available for roller machines |  |
| --- | --- | --- |
|  | Sanding Screen Fitted to rotary machines Attaches to disc drive with adhesive or Velcro Suitable for stripping any surface before applying seal or polish Available in different abrasive grades, lower grade numbers are more abrasive Also available for roller machines |  |
|  | Polishing Pad Fitted to rotary machines Made of polyester, non abrasive fibre Suitable for producing very high gloss Best results are achieved with a high speed machine |  |
|  | Cleaning Pad Fitted to rotary machines Made of nylon, with abrasive particles Suitable for spray cleaning any surface Suitable for medium to heavy soiled areas |  |

|  | Buffer Pad Fitted to rotary machines Made of none abrasive nylon Suitable for burnishing Will provide a high gloss finish |
| --- | --- |

BRUSHES AND PADS FOR CLEANING HARD AND SEMI HARD FLOORS (continued)

|  | Steel Wool Pad Fitted to rotary machines Made from wire wool Suitable for scouring semi hard floors Will provide a key for polish to stick to Ensure deep scratches are not left on surfaces as they will be seen through the final finish |  |
| --- | --- | --- |
|  | Bonnet Mop Fitted to rotary machines Made from wool, cotton or synthetic material Suitable for final burnishing Will give a highly polished finish |  |

SOLUTIONS AND CHEMICALS FOR CLEANING HARD AND SEMI HARD FLOORS

|  | Low Foam Detergent Used for single and double solution mopping Keeps the amount foam to a minimum Suitable for Terazzo, Marble and Stone |  |
| --- | --- | --- |
|  | Bactericide Disinfectant Destroys bacteria including MRSA, E. Coli. Ideal for all floors treated with emulsion polish Pleasantly fragranced and suitable for public areas |  |
|  | Deodorising Washroom Cleaner and Disinfectant Used for single and double solution mopping Contains Odour Neutralising Technology (ONT) Destroys germs and odours, ideal for toilet floors |  |
|  | Emulsion Stripper Used as a mop stripper or machine stripper Highly alkaline to penetrate through multiple polish coats Strips all types of emulsion floor polish Ideal for all alkali resistant hard floors |  |

|  | No Rinse Emulsion Speed Stripper Used as a mop stripper or machine stripper. Powerful solvent based stripper to remove heavy polish deposits Strips all types of emulsion floor polish, no rinsing necessary. Not suitable for wood floors or painted surfaces. |  |
| --- | --- | --- |

SOLUTIONS AND CHEMICALS FOR CLEANING HARD AND SEMI HARD FLOORS (continued)

|  | Polish Undercoat Porous floor sealer to aid durability and gloss of chosen polish. Ideal for sealing porous floors prior to polish application Improves final polish performance offering maximum protection |  |
| --- | --- | --- |
|  | High Solid Emulsion Polish Produces hard wearing, slip resistant high gloss finish Suitable for high traffic floors, scratch resistant Harnesses unique triple polymer technology |  |
|  | Satin Finish Floor Polish Low gloss floor polish enhances floor’s natural appearance Polymer, waxes and resins offer durable hard finish Traffic resistant with long lasting smooth finish |  |

|  | Buffable Floor Polish Polish that responds well to traditional buffing methods Water based giving high gloss finish Protects floor extending longevity |  |
| --- | --- | --- |
|  | Mop and Shine Polish Mop and bucket application ideal for small areas. Protects floors and maintains in single step. Suitable for all floors including sealed wood and linoleum. |  |

SOLUTIONS AND CHEMICALS FOR CLEANING HARD AND SEMI HARD FLOORS (continued)

|  | Floor Maintainer Used for single and double solution mopping Ideal for all floors treated with emulsion polish Pleasantly fragranced and can be buffed for shine |  |
| --- | --- | --- |
|  | Gloss Restoring Polish Water based polish for spray maintenance of floors Increases durability and buffs to give shine of floor. Ideal for repairing worn or scratched areas of floor polish. |  |
|  | Neutral Floor Cleaner for Scrubber Driers Water based with blend of non-ionic surfactants High dilution and low foaming for scrubber drier use Suitable for all protected and unprotected floors. |  |
|  | Alkaline Cleaner for Scrubber Driers Highly alkaline for optimum cleaning and degreasing High dilution and low foaming for scrubber drier use. Non fragranced facilitating use in food preparation areas |  |

|  | High Gloss Cleaner for Scrubber Driers Neutral cleaner with polymers and waxes. High dilution and low foaming for scrubber drier use. Enhances floor appearance and gives shine when buffed |  |
| --- | --- | --- |

SOLUTIONS AND CHEMICALS FOR CLEANING HARD AND SEMI HARD FLOORS (continued)

|  | Heavy Duty Liquid Wax Solvent and wax based floor polish. Ideal for maintenance of wood, cork, granwood & terracotta floors Cleans, protects and builds long lasting shine. |
| --- | --- |
|  | Water based seal for wood floors Acrylic and urethane formulation. Ideal for wood, cork or wood composition floors. Creates hard wearing protective seal extending floor longevity. |
|  | Solvent based seal for wood floors Neutral cleaner with polymers and waxes. High dilution and low foaming for scrubber drier use. Enhances floor appearance and gives shine when buffed |
|  | Broad Spectrum Disinfectant Destroys bacteria, virus, and fungi. Effective against Norwalk virus, MRSA, HIV, Avian Flu. Contains Accelerated Hydrogen Peroxide. Ideal for dealing with body spillages on carpet & hard floors. |

MACHINES AND EQUIPMENT FOR CLEANING HARD AND SEMI HARD FLOORS

Before using any Machine or Equipment the cleaner must understand the contents of the following sections of this See material.

A: Health & Safety, B: Identify Hazards & Security, and C: Reduce Risks

|  | Dustpan and Brush Used to manually pick up dust and dirt from floors Can be used to pick up smaller items of litter Suitable for all floors Long handles reduce the amount of kneeling required See section N1: Clean Floors Manually |  |
| --- | --- | --- |
|  | Dry Mop Sweeper Used to sweep dust and dirt from floors Can be used to gather up smaller items of litter before picking them up with a dustpan and brush Suitable for all hard floors Head swivels to allow figure of eight and snaking passes to be made over the floor See section N1: Clean Floors Manually |  |
|  | Dry Mop V Sweeper Used to sweep dust and dirt from floors Can be used to gather up smaller items of litter before picking them up with a dustpan and brush Suitable for all hard floors Size of V can be opened out to increase the width of the sweeping surface Dust is collected and transferred to the bottom of the V for easier control See section N1: Clean Floors Manually |  |
|  | Manual Damp Mop Used to apply wet solutions to floors, remove slurry and rinse Used with, mop buckets, wringer and mopping system Suitable for all hard floors Separate mops should be used for applying solution, removing slurry and rinsing See section N1: Clean Floors Manually |  |

MACHINES AND EQUIPMENT FOR CLEANING HARD AND SEMI HARD FLOORS (continued)

|  | Mop Bucket Used to hold solutions, clean water and slurry when manually wet cleaning floors Used with, mops, wringer and mopping system Suitable for all liquids Separate buckets should be used for holding solution, slurry and clean water See section N1: Clean Floors Manually |  |
| --- | --- | --- |

|  | Mop Wringer Used to squeeze liquids from mops when manually wet cleaning floors Used with, mops, buckets and mopping system Suitable for all mops Wringer should be positioned over the bucket containing slurry to ensure waste is not returned to solution or clean water bucket See section N1: Clean Floors Manually |  |
| --- | --- | --- |
|  | Mopping System A frame used to hold mops, buckets and wringers Used for manual wet mopping Fitted with castors so it is easy to move Reduces the amount of manual lifting when compared to using individual buckets, mops and wringers See section N1: Clean Floors Manually |  |
|  | Floor Scrapers Used to remove sticky solids from hard floors e.g. chewing gum, sticky tape Can be used to strip softened seal or polish Long handled scrapers reduce the amount of kneeling required |  |
|  | Edging Tool and Pads Used to scrub floor edges and corners where it is difficult for some rotary disc or drum machines to reach Different grades of abrasive pad are available to match the abrasive used on the rotary or drum cleaner Long handled tools reduce the amount of kneeling required |  |

MACHINES AND EQUIPMENT FOR CLEANING HARD AND SEMI HARD FLOORS (continued)

|  | Emulsion Polish Dish and Applicator Dish is used to hold polish so that the applicator can be placed into the polish Lambs wool pads can be removed from applicator for cleaning Long handles on dish and applicator reduce the amount of bending the cleaner has to do |  |
| --- | --- | --- |
|  | Squeegee A rubber blade, used to gather liquids from floor by scraping Suitable for use on any hard floor Most effective on smooth floors rather than contoured floors Can be used to spread stripper to floors |  |
|  | Sweeping Machine Fitted with brush head and has an internal suction cleaner Used to sweep and pick up dust, dirt and small sized litter Suitable for use on any hard or soft floor Position of brush allows cleaning right up to skirting boards For indoor use these machines are either electric cable or battery driven Can be walk behind or ride on type |  |
|  | Upright Rotary Scrubber Can be fitted with a wide range of brushes and pads Used to sweep, scrub, strip, grind, shampoo, polish and burnish Suitable for use on any floor Cannot reach into tight corners Can be used to wet or dry clean These machines are electric cable driven Can be fitted with solution tanks or used for spray cleaning Models are available with varying maximum speeds: Standard speed for stripping back High speed for general polishing Very high speed for high finish e.g. marble |  |

MACHINES AND EQUIPMENT FOR CLEANING HARD AND SEMI HARD FLOORS (continued)

|  | 14 Mini Rotary Scrubber Most suitable for steps and ledges Can be fitted with a wide range of brushes and pads Used to sweep, scrub, strip, grind, shampoo, polish and burnish Suitable for use on any floor Can reach further into tight corners than upright rotary scrubbers Can be used to wet or dry clean These machines are electric cable or battery driven Can be fitted with solution tanks or used for spray cleaning |  |
| --- | --- | --- |

|  | Cylindrical Scrubber Can be fitted with a wide range of cylindrical brushes Used to sweep, scrub, strip, grind Suitable for use on hard floors Difficult to reach into tight corners and up against skirting Can be used for wet cleaning These machines are electric cable or battery driven Can be fitted with solution tanks or used for spray cleaning |  |
| --- | --- | --- |

|  | Wet & Dry Suction Cleaner Used to suck loose dust, dirt and liquids from floors Suitable for use on any floor Can be fitted with a wide range of suction tool ends e.g. brushes, nozzles, squeegees Can be used to wet or dry clean Collected dust, dirt and liquids are stored in internal tanks These machines are electric cable Available as machines for wet suction or dry suction only Dry suction only machines MUST NEVER be used as wet suction machines as this can damage the machine |
| --- | --- |

MACHINES AND EQUIPMENT FOR CLEANING HARD AND SEMI HARD FLOORS (continued)

|  | Rotary Scrubber Dryer Is both a scrubber and wet suction machine Can be fitted with a wide range of brushes and pads Scrubber can be used to sweep, scrub, strip and rinse Has on board solution tanks and waste collection tanks Wet suction machine will squeegee and pick up slurry and waste. Suitable for use on hard floors Most suitable for wet cleaning For indoor use these machines are electric cable or battery driven. Available as ‘walk behind’ or ‘ride on’ models |  |
| --- | --- | --- |

# Text boxes

© B-Skill Ltd.

Permission to reproduce this material must be obtained from:

B-Skill Limited

Chaucer Buildings

57 Grainger Street

Newcastle upon Tyne

NE1 5JE

Tel: 0845 230 3736

Fax: 0845 230 4634

Designed in conjunction with Award Learning Services Ltd, Chelmsford

CLEANING BUILDING INTERIORS

Support Material for N/SVQ’s Level 2